## Slide 1
Figure 6. Distributed model underestimating during winter months.
For the precipitation data, station data is used which matches ERA5 well. The station data is averaged over the area by using Thiessen polygons. For evaporation data obtain from Global Land Evaporation Amsterdam Model (GLEAM) is used. Discharge station data is retrieved from USGS, the discharge of two stations in the lower part are added together.
The modelled runoff has some uncertainties due to the uncertainty in data, but also in the chosen parameters. The 8 model parameters are calibrated using Monte Carlo, trying all different combinations is very time consuming. Almost all parameters show a uniform distribution over the range against the NSE. So a parameter is easily taken for example as too low (when is practical it is higher), resulting in calibrating also the others wrong.
As can be seen, during the summer months the runoff is overestimated. Next to uncertainty, could the occurrence of reservoirs explain part of the overestimation. In figure 5 are the reservoirs shown which are classified in QGIS. Reservoirs are not taken into account in the model. Using a parameter in the model which reduces the fast flows in the summer, could result in a better fit.
Conceptual model of the Hudson River Basin
David Haasnoot and Anne Versleijen
River Basin Hydrology and Water Management
The aim is to describe the different elements of the water cycle within this region. To do so, data and information obtained from remote sensing techniques are used to develop a model.
The Hudson River Basin is located in the North East of the United States, which is around 35,000 km2. The lower part of the basin is an estuary. As the river in the lower part is influenced by the sea, only the Northern region is taken into account with an area of 20,000 km2. The region is showed in Figure 1. The area consists of forest, cropland and urban areas.
To model the water cycle in the basin, the HBV model is used. It is used both as lumped and distributed model. In the lumped model, the area is taken as homogenous. In the distributed model, the area is divided into wetland, hillslope and plateau areas.
The HBV model consists of various elements which describe different processes in the water cycle. If the air temperature is below 0.5 °C, the precipitation will be stored as snow. Otherwise it will intercept on vegetation until the storage capacity is reached. The excess (Pe) will flow into either the unsaturated rootzone or the fast reservoir. In case of melting snow, this flow will be added to Pe. From the unsaturated rootzone storage, water will leave as transpiration or percolate into the soil.
Introduction
HBV model
Data
Conclusion
Different data sets (data assimilation) voor evap. Uncertainty reduced
Results
HVB model (splitted in training (spinoff 1 year) and test)
Map with reservoirs
Sumax based on vegetation exercise
Objective
Results
The lumped HBV model is calibrated for 8 different parameters. The data is divided into sets of 4 years, each time the parameters are calibrated and than tested over the 4 following years. The Nash–Sutcliffe model efficiency coefficient (NSE) is calculated for each calibration, the closer to 1, the higher the predictive skill. The first 1.5 year are taken as spinoff and are not taken into account in calculating the NSE. For each calibration the same range of parameters is used. As can be seen in Figure 4, the NSE is decreasing over the years. Also the NSE of the test data is in most of the cases lower, with the largest difference in the years 1980-1983 and 1984-1987.
Figure 1. Considered upperpart of the Hudson River Basin. With dots, the different stations are depicted.
Figure 3. Data assimilation of precipitation (left) and evaporation (right) data.
Figure 2. HBV model which is used to model the water cycle in the Hudson River Basin.
Next to this, the distributed model under estimates the discharge during snowfall. The data is taken as average throughout the basin, but in practice it is a heterogenic area. For the distributed model, 21 parameters are needed. This leads to too much uncertainty to use the model for predictions.
Figure 5.Surface water areas classified by training in QGIS.
Figure 4. Results of lumped HBV model with highest NSE value.
Furthermore, both models have better outcome when same parameter range is chosen for the first 20 years based on the NSE. When run several times, the model of the past 20 years score always lower than data used from 1980 till 2000. Th uncertainty is large, but it is a remarkable observation.
To calculate both the NSE and the NSE log are used. When using NSE, the runoff is more calibrated towards the peaks, while using the log NSE the baseflow and timing is better modelled.
To improve modelling the peaks more data could be used. Further research could be done by executing multi-objective calibration. This will result in a model which both captures peaks and the base flows.
In this project, the model with highest NSE is chosen, while in practice this could not be the most useful model. Further research could be done by using generalized likelihood uncertainty estimation. Here, the NSE values are weighted and so are multiple solutions taken into account.