## Slide 1
For the precipitation data, station data is used.
Discharge data is retrieved from USGS.
For evaporation data obtain from Global Land Evaporation Amsterdam Model (GLEAM) is used.
The HBV model overestimates the discharge during summer. An explanation for this could be the occurence of reservoirs in the basin. (put figure of reservoirs?)
Next to this, the distributed model under estimates the discharge during snowfall. The data is taken as average throughout the basin, but in practice it is a heterogenic area. (plot where you can see this?)
Furthermore, both models have better outcome when same parameter range is chosen for the first 20 years based on the NSE. When excuceted several times, the model of the past 20 years score always lower than data used from 1980 till 2000.
Uncertainty is large,but it is remarkable. Because of large area  heterogeneity, average is taken
Data assmiliation part + plot
Conclusion
Reservoirs in basin  higher modelled outflow summer
Used factor to compensate
Distributed model: under estimates discharge during snowfall
Heterogenity
Average
Both lumped and distributed parameter range better outcome first 20 years, or last 20 years
Husdon basin modelled HBV upper
David Haasnoot and Anne Versleijen
River Basin Hydrology and Water Management
The aim is to describe the diferent elements of the water cycle within this region. To do so, data and information obtained from remote sensing techniques are used to develop a model.
The Hudson River Basin is located in the North East of the United States. The area is around 35,000 km2. The lower part of the basin is an estuary. Only the northern region is taken into account, as the river in the lower part is influenced by the sea. Figure basin + thiessen polygon? Discharge stations 2 stations summed up (area included)
To model the water cycle in the basin, the HBV model is used. It is used both as lumped and distributed model. In the lumped model, the area is taken as homogenous. In the distributed model, the area is divided into wetland, hillslope and plateau areas.
The HBV model consists of various elements which describe different processes in the water cycle. If the air temperature is below 0.5 °C, the precipitation will be stored as snow. Otherwise it will intercept on vegetation until the storage capacity is reached. The excess (Pe) will flow into either the unsaturated rootzone or the fast reservoir. In case of melting snow, this flow will be added to Pe. From the unsaturated rootzone storage, water will leave as transpiration or percolate into the soil.
Introduction
HBV model
Data
Conclusion
Different data sets (data assimilation) voor evap. Uncertainty reduced
Results
HVB model (splitted in training (spinoff 1 year) and test)
Map with reservoirs
Sumax based on vegetation exercise
Objective
Results
The lumped HBV model is calibrated for 8 different parameters. The data is divided into sets of 4 years, each time the parameters are calibrated and than tested over the 4 following years. Each time the , the Nash–Sutcliffe model efficiency coefficient (NSE) is calculated, the closer to 1, the higher the predictive skill. For each calibration the same range of parameters is used. As can be seen in Figure 3, the NSE is decreasing over the years.